## Slide 1
Chpapter 5: TRUSSES, FRAMES,
AND MACHINES

## Slide 2
TRUSSES

## Slide 4
USE OF TRUSS STRUCTURES IN AVIATION
4
A300,
Europe, 1972

## Slide 5
DIFFERENCE BETWEEN TRUSSES AND FRAMES
5
Connection by riveting,
moment-resistant

## Slide 6
DIFFERENCE BETWEEN TRUSSES AND FRAMES
Trusses | Frames
Members are subjected to tension/compression only | At least one member is subjected to bending, shear or torsion
Composed of rods | Composed of bars
Usually more simple to calculate, more weight effective | Usually more simple to manufacture, and to place in tight layout
6

## Slide 7
Plane truss
Space truss

## Slide 8: Frames
A frame
  has at least one multiforce member,
  is stationary,
  and is designed to support/resist loads.

## Slide 9: Machines
A machine
  has at least one multiforce member,
  is not stationary,
  and is designed to transmit loads from one thing to another.

## Slide 10: Definition of a Truss
Bolted or welded connections are assumed to be pinned together.
Only two-force members are considered.
When forces tend to pull the member apart, it is in tension. When the forces tend to compress the member, it is in compression.
A truss is a framework of members joined at ends with frictionless pins to form a stable structure.
Basic shape is a triangle.

## Slide 11: Types of Trusses

## Slide 12: Yet More Trusses http://www.caltruss.com/products.htm

## Slide 13
T
T
Tension Member
The free body diagram of a member shows that it is acted upon by two equal and opposite forces.
The hinged joint permits members to rotate with respect to each other and hence the members are subjected to purely axial forces.
A truss is held in position by the supports and the loads are applied only at joints.

## Slide 14
Compression Member
The convention for internal forces, i.e., the action of forces in the members on the joints is shown.
TENSION
COMPRESSION
C
C
T
C

## Slide 15
ANALYSIS & DESIGN ASSUMPTIONS
When designing both the member and the joints of a truss, first it is necessary to determine the forces in each truss member. This is called the force analysis of a truss. When doing this, two assumptions are made:
1. All loads are applied at the joints. The weight of the truss members is often neglected as the weight is usually small as compared to the forces supported by the members.
2. The members are joined together by smooth pins. This assumption is satisfied in most practical cases where the joints are formed by bolting the ends together.
With these two assumptions, the members act as two-force members. They are loaded in either tension or compression. Often compressive members are made thicker to prevent buckling.

## Slide 16
THE METHOD OF JOINTS (Section 6.2)
When using the method of joints to solve for the forces in truss members, the equilibrium of a joint (pin) is considered. All forces acting at the joint are shown in a FBD. This includes all external forces (including support reactions) as well as the forces acting in the members. Equations of equilibrium ( FX= 0 and  FY = 0) are used to solve for the unknown forces acting at the joints.
A free body diagram of Joint B

## Slide 17
STEPS FOR ANALYSIS
If the truss’s support reactions are not given, draw a FBD of the entire truss and determine the support reactions (typically using scalar equations of equilibrium).
2. Draw the free-body diagram of a joint with one or two unknowns. Assume that all unknown member forces act in tension (pulling the pin) unless you can determine by inspection that the forces are compression loads.
3. Apply the scalar equations of equilibrium,  FX = 0 and  FY = 0, to determine the unknown(s). If the answer is positive, then the assumed direction (tension) is correct, otherwise it is in the opposite direction (compression).
4. Repeat steps 2 and 3 at each joint in succession until all the required forces are determined.

## Slide 18: Method of Joints Example

## Slide 19: Method of Joints Example

## Slide 20: Zero Force Members (ZFMs)
TWO-Member Version
  When only TWO members form a NON-CoLinear truss joint and NO external load or support reaction is applied to the joint then the members MUST be ZERO-FORCE members.
THREE-Member Version
  When THREE members form a truss joint for which two of the members are CoLinear and the third is forms an angle with the first two, then the NON-CoLinear member is a ZERO-FORCE member provided NO external force or support reaction is applied to the joint
    NOTE that The CoLinear members carry EQUAL loads.

## Slide 21: Zero Force Members (ZFMs)
Truss members that canNOT carry load are called Zero Force Members.
Examples of Zero Force Members (ZFMs) are the colored members (AB, BC, and DG) in the truss shown at Right

## Slide 22: Zero Force Members (ZFMs)
Again Consider
FBD for AB & BC
Summing the forces in the y-direction in the AB FBD shows that FAB must be ZERO since it is NOT balanced by another y-force.
With FAB =0 Summing forces in the x-direction shows that FBC must also be zero

## Slide 23: Zero Force Members (ZFMs)
Again Consider
The FBD for DG
Summing forces in the y-direction in the DG free-body-diagram, reveals that FDG must be zero since it is not balanced by another y-force

## Slide 24
ZERO-FORCE MEMBERS (
You can easily prove these results by applying the equations of equilibrium to joints D and A.
If a joint has only two non-collinear members and there is no external load or support reaction at that joint, then those two members are zero-force members. In this example members DE, DC, AF, and AB are zero force members.
Zero-force members can be removed (as shown in the figure) when analyzing the truss.

## Slide 25
ZERO – FORCE MEMBERS (continued)
If three members form a truss joint for which two of the members are collinear and there is no external load or reaction at that joint, then the third non-collinear member is a zero force member.
Again, this can easily be proven. One can also remove the zero-force member, as shown, on the left, for analyzing the truss further.
Please note that zero-force members are used to increase stability and rigidity of the truss, and to provide support for various different loading conditions.

## Slide 26
There is a simple relationship between the number of joints (j) and the number of members (m) is established as
where,
m is number of members,
j represents the number of joints and
3 represents the external support reactions.
m = 2j-3

## Slide 27
If m = 2j – 3
If m < 2j – 3
If m > 2j – 3
Perfect truss
Deficient truss
Redundant truss

## Slide 28: Example 6.1
Determine the force in each member of the truss and indicate whether the members are in tension or compression.

## Slide 29: Solution
2 unknown member forces at joint B
1 unknown reaction force at joint C
2 unknown member forces and 2 unknown reaction forces at point A
For Joint B,

## Slide 30: Solution
For Joint C,
For Joint A,

## Slide 31: Solution
For Joint C,
For Joint A,

## Slide 32: Solution
FBD of each pin shows the effect of all the connected members and external forces applied to the pin
FBD of each member shows only the effect of the end pins on the member

## Slide 33
EXAMPLE
Check if there are any zero-force members.
First analyze pin D and then pin A
Note that member BD is zero-force member. FBD = 0
Why, for this problem, do you not have to find the external reactions before solving the problem?
Given: Loads as shown on the truss
Find: The forces in each member of the truss.
Plan:

## Slide 34
EXAMPLE (continued)
+   FX = – 450 + FCD cos 45° – FAD cos 45° = 0
+   FY = – FCD sin 45° – FAD sin 45° = 0
FCD = 318 lb (Tension) or (T)
and FAD = – 318 lb (Compression) or (C)
45 º
FCD
D
450 lb
FAD
FBD of pin D
45 º

## Slide 35
EXAMPLE (continued)
+   FX = FAB + (– 318) cos 45° = 0; FAB = 225 lb (T)
Could you have analyzed Joint C instead of A?
45 º
FAB
A
FBD of pin A
FAD
AY
Analyzing pin A:

## Slide 36
GROUP PROBLEM SOLVING
a) Check if there are any zero-force members.
Draw FBDs of pins D and E, and then apply EE at those pins to solve for the unknowns.
Note that Member CE is zero-force member so FEC = 0. If you didn’t see this simplification, could you still solve the problem?
Given: Loads as shown on the truss
Find: Determine the force in all the truss members (do not forget to mention whether they are in T or C).
Plan:

## Slide 37
GROUP PROBLEM SOLVING (continued)
Analyzing pin D: → + FX = 600 – FCD sin 26.57 = 0
FCD = 1341 N = 1.34 kN (C) (Note that FCD = FBC!)
+  FY = 1341 cos 26.57 – FDE = 0
FDE = 1200 N = 1.2 kN (T)
FBD of pin D
FDE
Y
D
600N
X
FCD
26.57
From geometry, tan-1(1/2)=26.57

## Slide 38
GROUP PROBLEM SOLVING (continued)
Analyzing pin E:
→ + FX = 900 – FEB sin 45 = 0
FEB = 1273 N = 1.27 kN (C)
+  FY = 1200 + 1273 cos 45 – FEA = 0
FEA = 2100 N = 2.1 kN (T)
FBD of pin E
FEA
Y
E
900 N
X
FEB
45
FDE

## Slide 39: Example  2D Truss
Using the method of joints, determine the force in each member of the truss.
SOLUTION PLAN
  Based on a free-body diagram of the entire truss, solve the 3 equilibrium equations for the reactions at E and C.
  Joint A is subjected to only two unknown member forces. Determine these from the joint (or pin) equilibrium requirements.
  In succession, determine unknown member forces at joints D, B, and E from pin equilibrium requirements.
  All member forces and support reactions are known at joint C. However, the joint equilibrium requirements may be applied to check the results

## Slide 40: Example  2D Truss
SOLUTION
  Based on a free-body diagram of the entire truss, solve the 3 equilibrium equations for the reactions at E and C.
So-Far, So-Good

## Slide 41: Example  2D Truss
Joint A is subjected to only two unknown member forces. Determine these from the pin (or joint) equilibrium requirements.
There are now only two unknown member forces at joint D.

## Slide 42: Example  2D Truss
There are now only two unknown member forces at joint B. Assume both are in tension.
There is one unknown member force at joint E. Assume the member is in tension.

## Slide 43: Example  2D Truss
CHECK
  All member forces and support reactions are known at joint C. However, the joint equilibrium requirements may be applied to check the results.


## Slide 44: A Real Truss Joint Idealized
2 in Tension, 3 in Compression

## Slide 45: 6.4 The Method of Sections
Used to determine the loadings within a body
If a body is in equilibrium, any part of the body is in equilibrium
To find forces within members, an imaginary section is used to cut each member into 2 and expose each internal force as external

## Slide 46: 6.4 The Method of Sections
Consider the truss and section a-a as shown
Member forces are equal and opposite to those acting on the other part – Newton’s Law

## Slide 47: 6.4 The Method of Sections
Procedure for Analysis
Free-Body Diagram
Decide the section of the truss
Determine the truss’s external reactions
Use equilibrium equations to solve member forces at the cut session
Draw FBD of the sectioned truss which has the least number of forces acting on it
Find the sense of an unknown member force

## Slide 48: 6.4 The Method of Sections
Procedure for Analysis
Equations of Equilibrium
Summed moments about a point
Find the 3rd unknown force from moment equation

## Slide 49: Example 6.5
Determine the force in members GE, GC, and BC of the truss. Indicate whether the members are in tension or compression.

## Slide 50: Solution
Choose section a-a since it cuts through the three members
Draw FBD of the entire truss

## Slide 51: Solution
Draw FBD for the section portion

## Slide 52
Sample problems 6.3
Determine the force in members FH, GH, and GI of the roof truss shown

## Slide 53
SOLUTION:
Take the entire truss as a free body. Apply the conditions for static equilib-rium to solve for the reactions at A and L.
tan α =
GL
15 m
8 m
FG
=
=
0.5333
α = 28.07º
30 m

## Slide 54
Pass a section through members FH, GH, and GI and take the right-hand section as a free body.
Apply the conditions for static equilibrium to determine the desired member forces.
Force in member GI

## Slide 55
Force in member FH
Force in member GH
15

## Slide 56: Space Trusses
An elementary space truss consists of 6 members connected at 4 joints to form a tetrahedron.
A simple space truss is formed and can be extended when 3 new members and 1 joint are added at the same time.
Equilibrium for the entire truss provides 6 additional equations which are not independent of the joint equations.
In a simple space truss, m = 3n − 6 where m is the number of members and n is the number of joints.
Conditions of equilibrium for the Ball-and-Socket joints provide 3n equations (no moments). For a simple truss, 3n = m + 6 and the equations can be solved for m member forces and 6 support reactions.

## Slide 57: 6.5 Space Trusses
Consists of members joined together at their ends to form 3D structure
The simplest space truss is a tetrahedron
Additional members would be redundant in supporting force P

## Slide 58: 6.5 Space Trusses
Assumptions for Design
Members of a space truss is treated as 2 force members provided the external loading is at the joints
When weight of the member is considered, apply it as a vertical force, half of its magnitude applied at each end of the member
Method of Joints
Solve ∑Fx = 0, ∑Fy = 0, ∑Fz = 0 at each joint
Force analysis has at least 1 unknown force and 3 unknown forces

## Slide 59: 6.5 Space Trusses
Method of Sections
When imaginary section is passes through a truss it must satisfied
∑Fx = 0, ∑Fy = 0, ∑Fz = 0
∑Mx = 0, ∑My = 0, ∑Mz = 0
By proper selection, the unknown forces can be determined using a single equilibrium equation

## Slide 60: Example 6.8
Determine the forces acting in the members of the space truss. Indicate whether the members are in tension or compression.

## Slide 61: Solution
For Joint A,

## Slide 62: Solution
For Joint B,
To show,