## Slide 1
Hydrology

## Slide 2
Hydrology
The flow of water across and through near surface environments

## Slide 4: Precipitation
Single strongest variable driving hydrologic processes
Formed by water vapor in the atmosphere
As air cools its ability to ‘hold’ water decreases and some turns to liquid or ice (snow)

## Slide 5
Causes of Precipitation

## Slide 6
Weather (day to day) vs. climate (years-decades and patterns)
What are hydrologists most concerned with?
Climate and geography result in biome classification
Weather vs. Climate Patterns

## Slide 7
Biomes and Rainfall

## Slide 8
Moisture Sources for USA
Notes: Figure 2.4-where does the moisture come from
Why does ohio get steady rainfall-fronts and convection
Compare to other areas in US

## Slide 10
Fig. 4.1
Evaporation & Transpiration

## Slide 11
Fig. 4.4

## Slide 12
Plant Transpiration
Most water absorption occurs in upper half of root zone

## Slide 13
Annual Pan Evaporation in USA

## Slide 14
Evaporating playa lake with salts around margin, eastern Washington

## Slide 17
Water Flow
Hillslope Hydrology
Runoff Processes:
    Horton overland flow
    Subsurface stormflow,
    Return flow
    Groundwater flow

## Slide 18
Factors Affecting Water Movement in Soils

## Slide 19
As we discuss mechanisms, remember…
  Many processes occur simultaneously
  Shifts can occur between processes in space and time
  Antecedent wetness conditions are important
  Watershed characteristic play a central role
Runoff Generation

## Slide 20
Horton overland flow occurs when the rainfall intensity exceeds the infiltration capacity
Horton Overland Flow

## Slide 22
Once thought to be the ONLY mechanism of runoff generation
Became coded into hydrologic models still in use today
Subsequent work showed role of partial source area where Saturation overland flow is produced
Horton Overland Flow

## Slide 23: Horton Overland Flow
If rainfall exceeds soil infiltration capacity:
  Water fills surface depression then
  Water spills over downslope as overland flow and
  Eventually to the stream

## Slide 24: Subsurface Stormflow
Lateral flow through soil above conductivity contrast.
Consists of both slower matrix flow and faster macropore flow

## Slide 25
Macropore flow,
Tennessee Valley,
California

## Slide 26: Saturation Overland Flow
Direct rainfall onto saturated areas.
Return flow from saturated soils in topographic lows and along valley bottoms where water table rises to intersect the surface.

## Slide 28
Overland flow, Tennessee Valley, California

## Slide 29
Overland flow, Tennessee Valley, California

## Slide 30
  Generally a minor contribution to runoff, why?
Direct Precipitation on Channels

## Slide 31
Groundwater & the Vadose Zone

## Slide 32
Groundwater Flow
Driven by hydraulic gradients
Q = K I A
K is hydraulic conductivity
A is cross sectional area
I is hydraulic gradient

## Slide 34
Hydrographs by Runoff Mechanism
Lag to peak
Throughflow
SOF
HOF
Peak Runoff
HOF
SOF
Throughflow

## Slide 38: Water balance of drainage basins
Net difference between precipitation and evaporation yields streamflow or groundwater recharge
Notes: The terms in the figure describe the hydrologic character of the basin.
Hydrologic data collection best carried out at the basin scale.

## Slide 39
Gaining and Losing Streams

## Slide 40
Watershed Urbanization